NBS

Specification text

NBS air-conditioning unit for horizontal installation in false ceilings. The housing of the NBS-100 consists of galvanised sheet steel profiles and heat and sound insulation. The housing of the NBS-150 consists of aluminium profiles, a jacket in sandwich design made of galvanised sheet steel, an interior heat and sound insulation, plastic corners and a circumferential seal. The motorised fan consists of a double-sided intake-operated centrifugal blower with built-in motor, heat exchanger register with galvanised steel frame, aluminium sheets and copper pipes. The filter element consists of a galvanised steel frame and a synthetic filter medium.

Models for operation with circulating air only or a mixture of processed fresh air and circulating air!

Manufacturer:	SCHAKO

Family: 			room air conditioning module NBS

Models NBS

Type

Room air conditioning module NBS	-NBS

Model

Model 100	-100

Model 150	-150

Size

Size 1 -1

Size 2 -2

Size 3 -3

System (water register version)

2-pipe register 2 pipe rows (heating or cooling)			-R2

2-pipe register 4 rows of pipes (cooling or heating)		-R4

4-pipe register 4 and 2 rows of pipes (cooling and heating)	-L4

Air filter

Air filter ISO Coarse 50%	-C5

Air filter ISO Coarse 60%	-C6

Filter removal

Filter removal in air flow direction on the left	-1

Filter removal in air flow direction on the right	-2

upwards										-3

downwards									-4

Flange

without flange								-F0

with supply air flange						-FZ

with return air flange						-FA

with supply air and return air flange		-FB

Water connection position

in air flow direction on the left			-W1

in air flow direction on the right			-W2

Droplet separator

without droplet separator	-T0

with droplet separator with polypropylene blades and a rack made of galvanised sheet steel	-T1

with droplet separator with polypropylene blades and a rack made of stainless sheet steel	-T2

Mixing unit

without mixing unit	-M0

with mixing unit in air flow direction on the left	-M1

with mixing unit in air flow direction on the right	-M2

Models FA-NBS (flexible connection to NBS)

Type

Flexible connection	-FA

Family

for room air conditioning module NBS	-NBS

Model

for product NBS-100	-100

for product NBS-150	-150

Size

Size 1 -1

Size 2 -2

Size 3 -3

Model

150 mm for supply air	-Z1

290 mm for supply air	-Z2

150 mm  for return air	-A1

150 mm  for return air	-A2

PL-NBS (plenum box for NBS)

Plenum box made of galvanised sheet steel

Type

plenum box	-PL

Family

for room air conditioning module NBS	-NBS

Model

for product NBS-100	-100

for product NBS-150	-150

Size

Size 1 -1

Size 2 -2

Size 3 -3

Model

supply air box	-Z

return air box	-A

Length

length xxxx mm	-xxxx

length 500 mm	-0500

Insulation

without insulation	-I0

thermal insulation of 10 mm	-I1

sound and thermal insulation of 20 mm	-I2

sound and thermal insulation of 40 mm	-I4

Connection in air flow direction

connection closed in air flow direction	-M00

connection open in air flow direction	-MAB

connecting flange in air flow direction	-MRE

connection with x spigot DN123 in air flow direction	-M1x

connection with x spigot DN158 in air flow direction	-M2x

connection with x spigot DN198 in air flow direction	-M3x

connection with x spigot DN248 in air flow direction	-M4x

Connection in air flow direction on the left

connection closed in air flow direction on the left	-L00

connection with x spigot DN123 in air flow direction on the left	-L1x

connection with x spigot DN158 in air flow direction on the left	-L2x

connection with x spigot DN198 in air flow direction on the left	-L3x

connection with x spigot DN248 in air flow direction on the left	-L4x

Connection in air flow direction on the right

connection closed in air flow direction on the right		-R00

connection with x spigot DN123 in air flow direction on the right	-R1x

connection with x spigot DN158 in air flow direction on the right	-R2x

connection with x spigot DN198 in air flow direction on the right	-R3x

connection with x spigot DN248 in air flow direction on the right	-R4x

ZMWS-NBS (baffle silencer for NBS)

Type

Accessories for baffle silencer MWS	-ZMWS

Family

for room air conditioning module NBS	-NBS

Model

for product NBS-100	-100

for product NBS-150	-150

Size

Size 1 -1

Size 2 -2

Size 3 -3

Model

contains MWK-MB sound-absorbing baffles. For use at a main interference frequency of 63 Hz and 500 Hz

-MB

contains MWK-OB sound-absorbing baffles. For use at a main interference frequency of 500 Hz and 8000 Hz	-OB

Length

length 1000 mm with a baffle length of 0500 mm	-1000

length 1250 mm with a baffle length of 0750 mm	-1250

length 1500 mm with a baffle length of 1000 mm	-1500

length 1750 mm with a baffle length of 1250 mm	-1750

length 2000 mm with a baffle length of 1500 mm	-2000

length 2250 mm with a baffle length of 1750 mm	-2250

length 2500 mm with a baffle length of 2000 mm	-2500

length 3000 mm with a baffle length of 2500 mm	-3000

Baffle thickness

baffle thickness 100 mm	-100

baffle thickness 200 mm	-200

Number of baffles

with xx baffles	-xx

Accessories

Pressure independent control valves

VPP46.10L0.2		-VC01

VPP46.10L0.4		-VC02

VPP46.15L0.2		-VC03

VPP46.15L0.6		-VC04

VPP46.20F1.4		-VC05

VPP46.25F1.8		-VC06

VPP46.32F4.0		-VC07

VPP46.10L0.2Q	-VC08

VPP46.10L0.4Q	-VC09

VPP46.15L0.2Q	-VC10

VPP46.15L0.6Q	-VC11

VPP46.20F1.4Q	-VC12

VPP46.25F1.8Q	-VC13

VPP46.32F4.0Q	-VC14

VPI46.15L0.2		-VC15

VPI46.15L0.6		-VC16

VPI46.20F1.4		-VC17

VPI46.25F1.8		-VC18

VPI46.32F4.0		-VC19

VPI46.15L0.2Q		-VC20

VPI46.15L0.6Q		-VC21

VPI46.20F1.4Q		-VC22

VPI46.25F1.8Q		-VC23

VPI46.32F4.0Q		-VC24

Actuators

SAST127474	-AT01

SAST127475	-AT02

SAPV127957	-AT03

SAPV128561	-AT04

SMPV132351	-AM01

SMPO132353	-AM02

Rotary drive for 6-way ball valve

GDB341.9E	-AR01

GDB161.9E	-AR02

GDB111.9E	-AR03

Room thermostat

RDG110			-TR01

RDG100			-TR02

RDG100T		-TR03

RDG100KN		-TK01

RDG160T		-TR05

RDG160KN		-TK02

6-way ball valve

VWG41.10-0.25-0.40	-V601

VWG41.10-0.25-0.65	-V602

VWG41.10-0.25-1.00	-V603

VWG41.10-0.40-0.65	-V604

VWG41.10-0.40-1.00	-V605

VWG41.10-0.40-1.30	-V606

VWG41.10-0.40-1.60	-V607

VWG41.10-0.65-1.00	-V608

VWG41.10-0.65-1.30	-V609

VWG41.10-0.65-1.60	-V610

VWG41.10-1.00-1.30	-V611

VWG41.10-1.00-1.60	-V612

VWG41.10-1.00-1.90	-V613

VWG41.10-1.30-1.60	-V614

VWG41.10-1.30-1.90	-V615

VWG41.10-1.60-1.90	-V616

VWG41.10-1.90-1.90	-V617

VWG41.10-0.25-1.30	-V618

VWG41.10-0.25-1.60	-V619

VWG41.10-0.25-1.90	-V620

VWG41.10-0.40-0.40	-V621

VWG41.10-0.40-1.90	-V622

VWG41.10-0.65-0.65	-V623

VWG41.10-0.65-1.90	-V624

VWG41.10-1.00-1.00	-V625

VWG41.10-1.30-1.30	-V626

VWG41.10-1.60-1.60	-V627

VWG41.20-0.65-2.50	-V628

VWG41.20-1.00-2.50	-V629

VWG41.20-1.60-2.50	-V630

VWG41.20-1.60-3.45	-V631

VWG41.20-2.50-3.45	-V632

VWG41.20-2.50-4.25	-V633

VWG41.20-4.25-4.25	-V634

VWG41.20-0.25-2.50	-V635

VWG41.20-0.25-3.45	-V636

VWG41.20-0.25-4.25	-V637

VWG41.20-0.40-2.50	-V638

VWG41.20-0.40-3.45	-V639

VWG41.20-0.40-4.25	-V640

VWG41.20-0.65-3.45	-V641

VWG41.20-0.65-4.25	-V642

VWG41.20-1.00-3.45	-V643

VWG41.20-1.00-4.25	-V644

VWG41.20-1.30-2.50	-V645

VWG41.20-1.30-3.45	-V646

VWG41.20-1.30-4.25	-V647

VWG41.20-1.60-4.25	-V648

VWG41.20-2.50-2.50	-V649

VWG41.20-3.45-3.45	-V650