Multi-Leaf Damper NK

Specification Text

Multi-leaf damper, consisting of dimensionally stable profiled frame made of 1.0 mm galvanised sheet steel, frame depth 120 mm, with joint flow-favouring hollow-body blades adjustable in opposite directions made of torsion-resistant aluminium profile.  Sealing airtight to DIN EN 1751 up to class 4. Housing leakage according to DIN EN 1751, class C, at a duct pressure of up to 1000 Pa, with locking device.

The blades are adjusted by means of external plastic gear wheels arranged on one side.

-	With plastic bearing, temperature-resistant up to +70 °C.

Product: SCHAKO type NK-SN-...-SV-M001-...

-	With sintered bearing, temperature-resistant up to +70°C.

Tested according to VDI 6022 Sheets 1+2, as well as DIN 1946 Sheet 2.

Product: SCHAKO type NK-SL-...-SV-M001-...

-	Damper position:

-	No spring return actuator (-NA) (standard)

-	Damper position:

-	Currentless OPEN - normally open (-NO)

-	Currentless CLOSED - normally closed  (-NC)

- 	only for actuators with spring return

-	Frame bore:

-	Without frame bore (-RB0)

-	With frame bore on two sides (-RB2)

Accessories:

-	Electric actuator

-	5 Nm, 24V AC/DC (-E044) / 230 V AC (-E045)

-	10 Nm, 24V AC/DC (-E047) / 230 V AC (-E048)

-	5 Nm, 0- 10 V DC 24 V AC/DC (-E046) / 230 V AC (-E016)

-	With 2 adjustable limit switches (-IS2)

-	10 Nm, 0- 10 V DC 24 V AC/DC (-E049) / 230 V AC (-E017)

-	With 2 adjustable limit switches (-IS2)

-	Spring return actuator 4 Nm, 24 V AC/DC (-E021)

-	Spring return actuator 10 Nm, 24 V AC/DC (-E027)

-	With 2 adjustable limit switches "CLOSED/OPEN" (-IS2)

-	Spring return actuator 4 Nm, 230 V AC (-E020)

-	Spring return actuator 10 Nm, 230 V AC (-E029)

-	With 2 adjustable limit switches "CLOSED/OPEN" (-IS2)

-	Spring return actuator 0-10 V, 4 Nm, 24 V AC/DC (-E023)

-	Spring return actuator 0-10 V, 10 Nm, 24 V AC/DC (-E028)