Ceiling impulse diffuser Model PIL

Specification texts

Square ceiling impulse diffuser for installation in supply and exhaust air systems in clean rooms, operating theatres and comfort rooms up to a height of 4 m.

Consisting of an easy to clean square perforated sheet steel front plate displaced with punch outs, painted RAL 9010 (white) or anodised aluminium in natural colour (natural colour anodised aluminium not available in the S model). The supply air model is additionally provided with a baffle plate and a sheet steel air guide funnel painted to RAL 9005 (black). It is fastened by concealed mounting (-VM) using a central fastening screw. TÜV inspected according to VDI 6022 Sheets 1+2, as well as DIN 1946 Sheet 2

Product: SCHAKO type PIL-N-QV-Z-...

-  for large air volumes: product: SCHAKO type PIL-G-QV-Z-...

-  star-shaped perforations (not possible in aluminium)

Product: SCHAKO type PIL-N-QS-Z-...

- for large air volumes

Product: SCHAKO type PIL-G-QS-Z-...-

-  Circular perforation (not possible in aluminium)

Product: SCHAKO type PIL-N-QK-Z-...

-  for large air volumes

Product: SCHAKO type PIL-G-QK-Z-...

-  Return air version without baffle plate and without air guide funnel Offset perforations

Product: SCHAKO type PIL-N-QV-A-...

-  Return air version without baffle plate and without air guide funnel star-shaped perforations (not possible in

aluminium)

Product: SCHAKO type PIL-N-QS-A-...

-  Return air version without baffle plate and without air guide funnel Circular perforation (not possible in

aluminium)

Product: SCHAKO type PIL-N-QK-A-...

-	with screw mounting (-SM), only for models with ball-impact guard (-BS) or in combination with a reduction

piece (-RF)

Round ceiling impulse diffuser for supply and return air systems in clean rooms, operating theatres and comfort rooms up to a height of 4 m.

Consisting of a round front plate easy to clean, with offset perforation, made of perforated sheet steel painted to RAL 9010 (white). The supply air model is additionally provided with a baffle plate and a sheet steel air guide funnel painted to RAL 9005 (black). It is fastened by concealed mounting (-VM) using a central fastening screw. TÜV inspected according to VDI 6022 Sheets 1+2, as well as DIN 1946 Sheet 2.

Product: SCHAKO type PIL-N-R...-Z-...

-  for large air volumes: product: SCHAKO type PIL-G-QV-Z-...

-  Star-shaped perforations. (not possible in aluminium)

Product: SCHAKO type PIL-N-RS-Z-...

-  for large air volumes

Product: SCHAKO type PIL-G-RS-Z-...

-  Circular perforation. (not possible in aluminium)

Product: SCHAKO type PIL-N-RK-Z-...

-  for large air volumes

Product: SCHAKO type PIL-G-RK-Z-...

-  Return air version without baffle plate and without air guide funnel Offset perforations.

Product: SCHAKO type PIL-N-RV-A-...

-  Return air version without baffle plate and without air guide funnel Star-shaped perforations. (not possible

in aluminium)

Product: SCHAKO type PIL-N-RS-A-...

-  Return air version without baffle plate and without air guide funnel Circular perforation. (not possible in

aluminium)

Product: SCHAKO type PIL-N-RK-A-...

Accessories:

-	Plenum box (SK-Q-... and SK-R-...) made of galvanised sheet steel, with fixing lugs.

-	Supply air model with integrated perforated straightener.

-	Return air model inside painted to RAL 9005 (black)

-	with damper (-DK1) in plenum box, adjustable from below, for simple air volume regulation without

dismounting the faceplate.

-	adjustable from below with cable (-DK2)

-	with volumetric flow meter (-VME1).

-	with ROB model (-ROB1), removable diffuser plate, damper and volumetric flow meter (only SK-Q-...)

-	with rubber lip seal (-GD1), at the connection spigot made of special rubber.

-	with thermal insulation

-	internal (-Ii)

-	external (-Ia)

-	Height of plenum box can be freely selected, xxx in mm, minimum height = spigot diameter + 102 mm

with SK-Q-... and spigot diameter +137 mm with SK-R-..., but at least 235 mm)

-	Spigot diameter can be freely selected, xxx in mm

-	Spigot position:

-	S0= spigot from above

-	S1= 1 lateral spigot on the box (standard)

-	S2= 2 spigots offset by 90°

-	S3= 2 spigots offset by 180°

-	S5 = 2 spigots arranged next to each other

-	Reduction piece made of galvanised sheet steel in the connection to ductwork (-RF), only for supply air

model without plenum box