Floor displacement air diffuser PILB

Specification texts

Floor displacement air diffuser in rectangular design, for installation in double floors, consisting of a rectangular faceplate with perforation and back-fitted support frame made of sheet steel painted to RAL 9005 (black).

Product: SCHAKO type PILB-...

-	Design:

-	square model (-Q)

-	rectangular design (-E)

-	Air throw:

-	one-way throw (-1)

-	two-way throw (-2)

-	Model:

-	faceplate with perforation d=5 mm (-A) (standard)

-	faceplate with perforation 8x8 mm (-B)

-	faceplate with perforation 12x5 mm (-C)

-	faceplate with perforation 18x6 mm (-D)

-	Length:

-	Length 300 mm (-0300) (only for PILB-Q-...)

(can only be combined with a 300 mm width)

-	Length 400 mm (-0400) (only for PILB-Q-...)

(can only be combined with a 400 mm width)

-	Length 500 mm (-0500) (only for PILB-Q-...)

(can only be combined with a 500 mm width)

-	Length 600 mm (-0600) (only for PILB-Q-...)

(can only be combined with a 600 mm width)

-	Length 1000 mm (-1000) (only for PILB-E-...)

(can be combined with any width)

-	Width:

-	150 mm (-150) (only for PILB-E-...)

-	300 mm (-300)

-	400 mm (-400)

-	500 mm (-500)

-	600 mm (-600)

-	Single / band design:

-	Single design (-N)

-	Material:

-	Stainless steel (V2A) (-V2)

-	 Paint:

-	Without paint (-0000)

-	Mounting:

-	without fastening (-00) (standard)

Accessories:

Dirt collection basket (-SFK0 / -SFK1)

-	without dirt collection basket (-SFK0) (standard).

-	with dirt collection basket (-SFK1), made of galvanised sheet steel (not for use with plenum box).

Installation frame (-ER0 / -ER1), without flange

-	without installation frame (-ER0) (standard).

-	with installation frame (-ER1), made of stainless steel 1.4301 (V2A) in the colour sand silver.

plenum box (-SK-...-73) (only for PILB-Q-...)

-	square model, for supply air (-Z) (not for use with dirt collection basket).

-	 Nominal size:

-	NW 300 (-300) (for diffuser LxB = 0300x300)

-	NW 400 (-400) (for diffuser LxB = 0400x400)

-	NW 500 (-500) (for diffuser LxB = 0500x500)

-	NW 600 (-600) (for diffuser LxB = 0600x600)

-	Mounting:

-	without fastening (-00) (standard)

-	Material:

-	made of galvanised sheet steel (-SV) (standard)

-	Damper

-	Without damper (-DK0) (standard)

-	with damper (-DK1), made of galvanised sheet steel, damper fastening made of plastic material, adjustable, in the plenum box housing, for simple air volume regulation.

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard)

-	with rubber lip seal (-GD1), made of special rubber, at the connection spigot.

-	Volumetric flow meter:

-	Without volumetric flow meter (-VME0) (standard)

-	ROB version:

-	without ROB version (-ROB0) (standard)

-	Insulation:

-	without insulation (-I0) (standard)

-	with internal insulation (-Ii), thermal insulation inside the plenum box.

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	standard height of plenum box (-KHS)

-	Height of plenum box in mm, freely selectable (-xxx) (minimum height [KHS] = spigot diameter øD + 72 mm, but at least 170 mm, always with 3 digits)

-	Spigot diameter:

-	Standard spigot diameter (-SDS)

-	Spigot diameter in mm, freely selectable (-xxx, always with 3 digits).

-	Spigot position:

-	1 lateral spigot on the plenum box (-S1) (standard)

-	2 spigots offset by 90° (-S2)

-	2 spigots offset by 180° (-S3)

-	2 spigots arranged next to each other (-S5)

plenum box (-AK-...-52) (only for PILB-E-...)

-	rectangular model, for supply air (-Z), in single design (-N), installation without fastening (-00) (not for use with dirt collection basket).

-	Length:

-	Length 1000 mm (-1000) (can be combined with any width)

-	Width:

-	Width: 150 mm (-150) / 300 mm (-300) / 400 mm (-400) / 500 mm (-500) / 600 mm (-600)

-	Material:

-	made of galvanised sheet steel (-SV) (standard)

-	Damper

-	Without damper (-DK0) (standard)

-	with damper (-DK1), made of galvanised sheet steel, damper fastening made of plastic material, adjustable, in the plenum box housing, for simple air volume regulation.

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard)

-	with rubber lip seal (-GD1), made of special rubber, at the connection spigot.

-	Insulation:

-	without insulation (-I0) (standard)

-	with internal insulation (-Ii), thermal insulation inside the plenum box.

-	with external insulation (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	standard height of plenum box (-KHS)

-	Height of plenum box in mm, freely selectable (-xxx) (minimum height [KHS] = spigot diameter øD +62 mm, but at least 200 mm, always with 3 digits)

-	Spigot diameter:

-	Standard spigot diameter (-SDS)

-	Spigot diameter in mm, freely selectable (-xxx, always with 3 digits).

-	Spigot position:

-	1 lateral spigot on the plenum box (-S1) (standard)

-	1 spigot front side (available only upon request)