Floor displacement air diffuser PILBR

Specification texts

Floor displacement air diffuser, in round design, for installation in double floors, consisting of a round faceplate made of stainless steel (V2A) without paint (-V2-0000), with radial perforation and back-fitted baffle plate. Baffle plate made of sheet steel painted to RAL 9005 (black) for PILBR-200 and of plastic material similar to RAL 9005 (black) for PILBR-250.

Product: SCHAKO type PILBR

-	 Nominal size:

-	NW 200 (-200)

-	NW 250 (-250)

-	Mounting:

-	without fastening (-00)

-	with fastening prongs (-BK) (standard), made of galvanised sheet steel.

-	Concealed mounting (-VM) (at an extra charge), (fastened to the plenum box by means of the central screw M6x120 (according to DIN EN ISO 4762) (only available with plenum box -SK))

Accessories:

Dirt collection basket (-SFK0 / -SFK1)

-	without dirt collection basket (-SFK0) (standard).

-	with dirt collection basket (-SFK1), made of galvanised sheet steel (not for use with plenum box).

Mounting ring (-ER0 / -ER1) with flange

-	without mounting ring (-ER0) (standard).

-	with mounting ring (-ER1), made of stainless steel 1.4301 (V2A) in the colour sand silver.

Plenum box (-SK-...-53)

-	square model (-Q), for supply air (-Z) (not for use with dirt collection basket).

-	 Nominal size:

-	NW 200 (-200)

-	NW 250 (-250)

-	Mounting:

-	without fastening (-00) (standard)

-	Concealed mounting (-VM) (at an extra charge)

-	Material:

-	made of galvanised sheet steel (-SV) (standard)

-	Damper

-	Without damper (-DK0) (standard)

-	with damper (-DK1), made of galvanised sheet steel, damper fastening made of plastic material, adjustable, in the plenum box housing, for simple air volume regulation.

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard)

-	with rubber lip seal (-GD1), made of special rubber, at the connection spigot.

-	Volumetric flow meter:

-	Without volumetric flow meter (-VME0) (standard)

-	ROB version:

-	without ROB version (-ROB0) (standard)

-	Insulation:

-	without insulation (-I0) (standard)

-	With box insulation inside (-Ii), thermal insulation at the inside of the plenum box.

-	with box insulation outside (-Ia), thermal insulation at the outside of the plenum box.

-	Height of plenum box:

-	standard height of plenum box (-KHS)

-	Height of plenum box in mm, freely selectable (-xxx) (minimum height [KHS] = spigot diameter øD + 57 mm, but at least 180 mm, always with 3 digits)

-	Spigot diameter:

-	Standard spigot diameter (-SDS)

-	Spigot diameter in mm, freely selectable (-xxx, always with 3 digits).

-	Spigot position:

-	1 lateral spigot on the plenum box (-S1) (standard)