Flexible Duct Silencer Model RS-F

Specification texts

Flexible duct silencer for reducing flow generated noise consisting of 2-layer aluminium outer tube with galvanised end caps. Connection to the duct pipeline via connection pieces made of galvanised sheet steel. Aluminium inner tube perforated. Temperature-resistant up to 200°C. Sound-absorbing material made of synthetic-resin-bonded glass wool, comprising an abrasion-resistant, filament-reinforced tube inner wall. Non-flammable according to DIN 4102, construction material class A1,

Product: SCHAKO type RS-F

-	Length:

-	500 mm (-0500)

-	1000 mm (-1000)

-	1500 mm (-1500)

-	2000 mm (-2000)

-	Packing thickness:

-	25 mm (...-25)

-	50 mm (...-50)

Accessories:

-	Rubber lip seal (-GD1) on both sides, made of special rubber.