Duct Silencer Model RS

Specification texts

Duct silencer type RS with sound absorption according to the absorption principle, by means of an annular chamber filled with mineral wool according to DIN 4102 A2 non-flammable, mineral wool with glass silk cover. Consisting of 1.0 mm thick outer jacket with a perforated plate covered in abrasion-resistant manner toward the air flow direction. Connection to the duct via 50 mm long connection pieces.

Duct silencers have been tested according to DIN EN 1751:2014 tightness class “C”.

Product: SCHAKO type RS-N-...

-	additionally with central baffle with mineral wool filling and glass

silk cover.

Product: SCHAKO type RS-M-...

-	Outer jacket, perforated sheet, connection piece and central baffle made of:

-	Galvanised sheet steel (-SV)

-	Packing thickness:

-	50 mm (...-50)

-	100 mm (...-100)

-	150 mm (...-150)

-	Baffle thickness

-	without central baffle (only possible with model RS-N)(-000)

-	60 mm (-060)

-	75 mm (-075)

-	100 mm (-100)

-	150 mm (-150)

Accessories:

-	Metu flange (-MF1), on both sides, duct flange AF

-	Counter flange (-GF1) (pair), loose, on both sides, only possible for Metu flange

-	Tension ring (-SR1) (pair), loose, to connect Metu flange to counter flange

-	Flat flange (-FF1), on both sides, according to DIN 24 154/5, only possible without counter flange, not possible for NW 71, 90, 112 and 350

-	Rubber lip seal (-GD1), on both sides, made of special rubber