Step Swirl Diffuser SAR/SAQ/SARP

Specification texts

Step swirl diffuser for micro-air-conditioning, suitable for vertical installation in steps, consisting of a round swirl diffuser plate of stove-enamelled sheet steel painted to RAL 9010 (white) and quick-installation mounting ring, made of stove-enamelled sheet steel in the colour of the faceplate. In order to achieve an extremely rapid reduction of the air velocity and the temperature difference, the non-adjustable, radially arranged air deflection blades produce a highly inductive air throw. NW 060 with spring mounting (-FM).

Product: SCHAKO type SAR-060-...

Step swirl diffuser for micro-air-conditioning, suitable for vertical installation in steps, consisting of a round swirl diffuser plate made of sheet steel stove-enamelled to RAL 9010 (white) and quick-installation mounting ring with integrated series resistor for building up a pre-pressure, made of sheet steel stove-enamelled in the colour of the faceplate, for NW 110 made of plastic similar to RAL colour 9005 (black). Non-adjustable radial air deflection blades create a highly inductive throw for quick reduction of air velocity and temperature difference. NW 110 and 150 available with screw mounting (-SM) or concealed mounting (-VM) (at an extra charge). NW 150 also available with fastening prongs (-BK) (at an extra charge). NW 150 with inlet connection spigot plus connection spigot DN80 (-A1) or connection spigot DN125 (-A2).

Product: SCHAKO type SAR-...

Step swirl diffuser for micro-air-conditioning, suitable for vertical installation in steps, in panel design with integrated swirl diffusers NW 060 or NW 110, made of sheet steel stove-enamelled to the colour of the faceplate. Rectangular faceplate, 2-7 diffusers per faceplate possible. Non-adjustable radial air deflection blades create a highly inductive throw for quick reduction of air velocity and temperature difference. With screw mounting (-SM) or concealed mounting (-VM, standard).

Product: SCHAKO type SARP-...

Step swirl diffuser for micro-air-conditioning, suitable for vertical installation in steps, consisting of a square swirl diffuser plate made of stove-enamelled sheet steel RAL 9010 (white) and

quick-installation mounting ring with integrated series resistor for building up a pre-pressure, made of plastic, similar to RAL colour 9005 (black). In order to achieve an extremely rapid reduction of the air velocity and the temperature difference, the non-adjustable, radially arranged air deflection blades produce a highly inductive air throw. NW 110 with screw mounting (-SM) or concealed mounting (-VM) (at an extra charge).

Product: SCHAKO type SAQ-110-...