Step Impulse Diffuser Model SIA

Specification texts

Step impulse diffuser with high induction factor for vertical installation in steps in pressure floors. The main fields of application are concert halls, auditoria , theatres, and cinemas for air-conditioning. Consisting of a rectangular diffuser plate made of sheet steel painted to RAL 9010 (-9010, white) or RAL 9005 (-9005, black) with a circumferential frame made of extruded aluminium profile painted to the same colour as the diffuser plate. With integrated guiding plate for building up an initial pressure, made of galvanised sheet steel painted to RAL colour 9005 (black). Ingenious fittings on the inside rapidly reduce speed and temperature between the diffuser and the legs. Fixing with concealed mounting (-VM).

Product: SCHAKO type SIA

Air throw

-	Supply air (with air diffuser plate) type SIA-Z

-	Return air (without air diffuser plate) type SIA-A

End pieces

-	Without end piece (-EO)

-	Mounted on both sides (-EB)(supplied loose)

-	Mounted on the left (-EL)(mounted ex works)

-	Mounted on the right (-ER)(mounted ex works)