Poppet valve STV

Specification text

Poppet valve for supply air, consisting of a round sheet steel front frame (-SB) painted to RAL colour 9010 (white)

(-9010, standard) or painted to a freely selectable RAL colour       (-xxxx, always with 4 digits), with circumferential foam seal. With adjustable valve disc made of sheet steel (painted to the colour of the front frame), for air volume regulation. Counter nut for securing the air volume setting and threaded spindle made of galvanised steel.

With mounting ring made of galvanised sheet steel and bay-onet catch (for mounting the poppet valve to the mounting ring). Mounting ring fastening to the ceiling by means of screw mounting (-SM), with mounting bracket.

Product: SCHAKO type STV-Z-...

--	Poppet valve for return air, with adjustable valve disc.

Product: SCHAKO type STV-A-...

Accessories (at an extra charge):

---	Panelled cover plate (-PA), made of sheet steel, painted to the colour of the poppet valve (mounting ring 	is firmly fitted to the panelled cover plate).

--- Saddle bracket (-SA), made of galvanised sheet steel (mounting ring is firmly fitted to the saddle bracket).