Smoke Detection System Model SVA-FS

Specification texts

Fire damper poppet valve (shut-off device) for supply and return air, with thermal trigger (72 °C) and adjustab-le valve plate for air volume regulation.

Resistance class K90, with ventilation duct made of non-flammable building materials connected on one side.

When connected to flammable ventilation ducts, its re-sistance class is K 30.

The fire damper poppet valve may be fitted in walls ma-de of masonry to DIN 1053 with a thickness of ≥ 115 mm or concrete with a thickness of ≥ 100 mm and in ceilings made of concrete with a thickness of ≥ 100 mm. This is also valid for duct walls and walls from vertical ventilation ducts.

Housing, shut-off plate and wall sleeve made of painted sheet steel, colour RAL 9010 (white).

Manual trigger on valve disc. Valve fixing at the wall sleeve with bayonet fixing.

Approval certificate number: Z-41.3-312

Product: SCHAKO type SVA-FS

- NG 100

- NG 150

Accessories:

- Extension spigot made of galvanised sheet steel

Alternative model (upon request and at an extra charge)

RAL colours