Excess Pressure Flap UEKU

Specification texts

Excess pressure flap type UEKU consisting of a stable U frame made of galvanised steel, with blades made of aluminium profile (natural aluminium), self-opening and -closing.

Product: SCHAKO type UEKU-AL-...

Width:

-	400 mm (-0400)

-	500 mm (-0500)

-	600 mm (-0600)

-	800 mm (-0800)

-	900 mm (-0900)

-	1000 mm (-1000)

-	Width in mm, freely selectable (-xxxx) (400 £ width £ 1000) (always with 4 digits).

Height:

-	260 mm (-0260)

-	345 mm (-0345)

-	425 mm (-0425)

-	510 mm (-0510)

-	675 mm (-0675)

-	760 mm (-0760)

-	840 mm (-0840)

-	1005 mm (-1005)

-	Height in mm, freely selectable (-xxxx) (260 £ height £ 1005) (always with 4 digits).

Frame bore:

-	without frame bore (-RB0)

-	With frame bores on both sides (-RB2).