Specification text VMPR

Round model

Mechanical volumetric flow controller type VMPR, in round design, position-independent installation, for constant volumetric flow control up to a max. differential pressure of 1000 Pa, for duct connection to DIN EN 1506. Housing and control damper made of galvanised sheet steel (-SV), control housing made of plastic.

Product: SCHAKO type VMPR

NW ......................................

Housing and control damper (at an extra charge) made of:

---	Galvanised sheet steel with DD-coating (-DD)

---	Stainless steel 1.4301 (-V2)

---	Stainless steel 1.4571 (-V4)

Control housing (at an extra charge) made of:

---	Stainless steel 1.4301 (-V2)

---	Stainless steel 1.4571 (-V4)

Accessories (at an extra charge)

---	Acoustic cladding (-DS2), made of 20 mm sound-absorbing material, non-flammable according to DIN 4102-17, with sheet metal casing.

---	Flat-bed acoustic cladding (-FD1), made of 3 mm sound-absorbing material with sheet metal casing.

---	METU flange (-MF1/-MF2), on both sides, duct flange AF.

---	Counter flange (-GF) (pair), loose, on both sides, for METU flange.

---	Tension ring (-SR) (pair), loose, for connecting the METU flange to the counter flange.

---	Flat flange (-FF1/-FF2), on both sides, according to DIN 24 154 / 5, made of the same material as the housing.

---	Rubber lip seal (-GD1), on both sides, made of special rubber, silicone-free.

---	Duct silencer (-RS), outer casing and perforated plate made of galvanised sheet steel or stainless steel 1.4301 (V2A) or 1.4571 (V4A) (at an extra charge), with mineral wool filling.

---	Electric actuator (-E), 3-point control (standard, VMPR-…-E044; 24 V, VMPR-…-E045; 230 V) or constant control

(VMPR-…-E046; 24 V, VMPR-…-E016; 230 V), for adapting the supply air and return air volume to varying room occupations.

VMPQ specification text

Rectangular model

Mechanical volumetric flow controller type VMPQ, in rectangular design, right-hand model, for constant volumetric flow control up to a max. differential pressure of 1000 Pa, for duct connection to DIN EN 1505. Housing and control damper made of galvanised sheet steel (-SV), control housing made of plastic.

Product: SCHAKO type VMPQ

Size ................. x ................. (width x height)

Housing and control damper (at an extra charge) made of:

---	Galvanised sheet steel with DD-coating (-DD)

---	Stainless steel 1.4301 (-V2)

---	Stainless steel 1.4571 (-V4)

Control housing (at an extra charge) made of:

---	Stainless steel 1.4301 (-V2)

---	Stainless steel 1.4571 (-V4)

Accessories (at an extra charge):

---	Acoustic cladding (-DS2) made of 20 mm sound-absorbing material, non-flammable according to DIN 4102-17, with sheet metal casing and M6 cage nuts.

---	Mineral wool silencer (-ZSQ) with METU profile M2 on both sides , housing (L=1500) made of galvanised sheet steel or stainless steel 1.4301 (V2A) or 1.4571 (V4A) (at an extra charge), with integrated MWK sound-absorbing baffles (L=1000). The MWK silencing baffles with RAL quality seal consist of abrasion-resistant mineral fibre boards covered with fibre glass filament (biosoluble, non-flammable to DIN 4102) in a frame made of the same material as the mineral wool silencer housing. Baffles measured to ISO/DIS 7235 and to DIN 45646.

---	Electric actuator (-E), 3-point control (standard, VMPQ-…-E044; 24 V, VMPQ-…-E045; 230 V) or constant control (VMPQ-…-E046; 24 V, VMPQ-…-E016; 230 V), for adapting the supply air and return air volume to varying room occupations.