Long throw nozzle grille WGA

Specification texts

Long throw nozzle grille type WGA-Q-F0-… particularly sui-table for air-conditioning of high and large rooms such as multi-purpose halls. High-induction supply air intake through several nozzles of high throw speeds at low sound power le-vel, to achieve long throws and efficient throw pattern through optimum nozzle shape.

High flexibility through a wide range of installation options. Installation in walls, ceilings, plenum boxes and ducts. Coo-ling and heating modes are possible. Suitable for use in 100% to 40% VAV systems. Housing consisting of sheet steel painted with a high-quality powder coating to a RAL colour (RAL 9010 [white, standard], RAL 9005 [black], RAL 9006 [white aluminium], RAL 9007 [grey aluminium] or a freely selectable RAL colour). Fixed nozzles made of plastic, similar to RAL colour RAL 9010 (-DW, white, standard), RAL 9005 (-DS, black), RAL 9006 (-DA, white aluminium) or RAL 9007 (-DG, grey aluminium). With visible screw fixing (standard, -SM) or concealed mounting (-VM).

Product: SCHAKO type WGA-Q-F0-...

-	Installation in walls, ceilings, plenum boxes and ducts, with individually manually adjustable nozzles, 	pivoting range 45°, without change in the sound power level and pressure loss upon adjustment. With 	visible screw fixing (standard, -SM) or concealed mounting (-VM).

Product: SCHAKO type WGA-Q-V0-...

-	Installation in walls, ceilings, plenum boxes and ducts, with jointly manually adjustable nozzles, pivoting 	range 34°, without change in the sound power level and pres-sure loss upon adjustment. With visible 	screw fixing (-SM).

Product: SCHAKO type WGA-Q-VG-...

-	Installation in walls, ceilings, plenum boxes and ducts, with jointly motor-adjustable nozzles, pivoting 	range 34°, without change in the sound power level and pressure loss upon adjustment. With visible 	screw fixing (-SM).

With electric actuator:

-	3-point activation (-E080) 230 V AC

-	Actuator signal Y, 24 V AC, 0-10 V DC (-E081) (stan-dard)

-	3-point activation (-E082) 24 V AC.

Product: SCHAKO type WGA-Q-VE-...

-	Installation in walls, ceilings, plenum boxes and ducts, with nozzles jointly adjustable via thermocouple, 	pivoting range 34°, without change in the sound power level and pressure loss upon adjustment - without 	electrical ener-gy. At a supply air temperature of 20 °C or lower, the nozzles are in the cooling position 	with throw direction diagonally upwards (max. angle 17°). At a supply air temperature of 35 °C or higher, 	the nozzles are in the he-ating position with throw direction diagonally upwards (max. angle -17°). In the 	temperature range between 20 °C and 35 °C, the nozzle row is adjusted linearly. With vi-sible screw 	fixing (-SM).

Product: SCHAKO type WGA-Q-VT-...

-	as a band (-B) (only possible for WGA-Q-F0-… / WGA-Q-V0-…)

-	2-part (BL ≤ 2025)

-	multi-part (BL > 2025)

Accessories:

-	with ball-impact guard (-BS), integrated into the housing made of profiled steel (powder-coated in the 	same co-lour as the housing).

-	with hit-and-miss damper (-SS) for volumetric flow ad-justment, adjustable on room side, made of 	electrolyti-cally galvanized sheet steel (not possible in connection with AK and VM).

-	with plenum box (-AK) made of galvanized sheet steel, with lateral connection spigot

-	with damper (-DK1) in plenum box, adjustable from below, for simple air volume regulation without 		dismounting the grille.

-	with rubber lip seal (-GD1), on plenum box, made of special rubber.

-	with thermal insulation

-	internal (-li)

-	external (-la)

-	VM counter pole brace made of galvanised sheet steel.

-	VM counter pole brace (-GT, pair), made of galvanised sheet steel (only possible in the absence of AK, 	only pos-sible for WGA-Q-F0-… and WGA-Q-V0-…).

Long throw nozzle grille type WGA-R-F0-… particularly sui-table for air-conditioning of high and large rooms such as multi-purpose halls. High-induction supply air intake through several nozzles of high throw speeds at low sound power le-vel, to achieve long throws and efficient throw pattern through optimum nozzle shape.

Installation in round ducts. Cooling and heating modes are possible. Suitable for use in 100% to 40% VAV systems. Hou-sing consisting of sheet steel painted with a high-quality powder coating to a RAL colour (RAL 9010 [white, standard], RAL 9005 [black], RAL 9006 [white aluminium], RAL 9007 [grey aluminium] or a freely selectable RAL colour). Fixed nozzles made of plastic, similar to RAL colour RAL 9010 (-DW, white, standard), RAL 9005 (-DS, black), RAL 9006 (-DA, white aluminium) or RAL 9007 (-DG, grey aluminium). With visible screw fixing (-SM).

Product: SCHAKO type WGA-R-F0-...

-	Installation in round ducts, with individually manually ad-justable nozzles, pivoting range 45°, without 	change in the sound power level and pressure loss upon adjust-ment. With visible screw fixing (-SM).

Product: SCHAKO type WGA-R-V0-...

-	Installation in round ducts, with jointly manually ad-justable nozzles, pivoting range 34°, without change in 	the sound power level and pressure loss upon adjustment With visible screw fixing (-SM).

Product: SCHAKO type WGA-R-VG-...

-	Installation in round ducts, with jointly motor-adjustable nozzles, pivoting range 34°, without change in the 	sound power level and pressure loss upon adjustment. With vi-sible screw fixing (-SM).

With electric actuator:

-	3-point activation (-E080) 230 V AC.

-	Actuator signal Y, 24 V AC, 0-10 V DC (-E081) (stan-dard)

-	3-point activation (-E082) 24 V AC.

Product: SCHAKO type WGA-R-VE-...

-	Installation in round ducts with nozzles jointly adjustable via thermocouple, pivoting range 34°, without 	change in the sound power level and pressure loss upon adjustment - without electrical energy. At a 	supply air temperature of 20 °C or lower, the nozzles are in the cooling position with throw direction 	diagonally upwards (max. angle 17°). At a supply air temperature of 35 °C or higher, the nozzles are in 	the heating position with throw direction diagonally upwards (max. angle -17°). In the temperature range 	between 20 °C and 35 °C, the nozzle row is ad-justed linearly. With visible screw fixing (-SM).

Product: SCHAKO type WGA-R-VT-...

Accessories:

-	with ball-impact guard (-BS), integrated into the housing made of profiled steel (powder-coated in the 	same co-lour as the housing).

-	with hit-and-miss damper (-SS) for volumetric flow ad-justment, adjustable on room side, made of 	electrolyti-cally galvanized sheet steel. (not possible in connection with AK).