Wall Displacement Diffuser Model WQA

Specification texts

Wall displacement diffuser type WQA with removable perforated sheet steel faceplate for easy cleaning according to VDI 6022. Suitable for low-turbulence supply air entry at low air entry velocities. Consisting of housing and faceplate made of galvanised sheet steel (standard), sheet steel painted to RAL 9010 (white) or stainless steel painted in the colour sand silver. To achieve even air distribution, a removable synthetic fibre filter mat, alternatively an air diffuser plate made of perforated sheet steel, is installed. The displacement diffuser can also be provided with a high-quality powder coating in a RAL colour. Suitable for installation in or to walls.

-	with round connection spigot

Product: SCHAKO type WQA-R-...

-	with rectangular connection spigot

Product: SCHAKO type WQA-K-...

Models:

-		WQA-...-O-...:	Top connection spigot

-		WQA-...-U-...:	Bottom connection spigot

-		WQA-...-H-...:	Rear connection spigot

-		WQA-...-L-...:	Connection spigot on the left-hand side

-		WQA-...-R-...:	Connection spigot on the right-hand side

-		WQA-...-...-FT-...:	with filter pocket (standard)

-		WQA-...-...-LV-...:	with air diffuser plate (standard for WQA-...-H).

-		WQA-...-H-FV-...:	with filter mat

Accessories:

-		Rubber lip seal (-GD1), made of special rubber (WQA-R-... only).

-		Hit-and-miss damper (-SS) for simple air volume regulation (WQA-K-.... only).

-		Throttling element (-DV1) for simple air volume regulation (WQA-R-... only).