Round Duct System Accessories RD Accessories

Specification texts

-	Dummy pipe (-BLR)

-	Pressed bend (-BGE)

-	Bent segment (-BSE)

-	Symmetric reduction piece (-USE)

-	Asymmetric reduction piece (-UAE)

-	T-piece 90° (-ATE)

-	Push-on rosette (SRO)

-	Straight end cover (-EG)

-	Connection sleeve (-MUF)

Dummy pipe BLR according to DIN EN1506, suitable for connection to DIN ducts.

Product: SCHAKO type BLR-...

-	Nominal width:

-	NW 200 (-200)

-	NW 224 (-224)

-	NW 250 (-250)

-	NW 280 (-280)

-	NW 315 (-315)

-	NW 355 (-355)

-	NW 400 (-400)

-	NW 450 (-450)

-	NW 500 (-500)

-	Length:

-	1-part:

500 mm / 750 mm / 1000 mm (-0500 / -0750 / -1000).

-	2-part:

1500 mm / 1750 mm / 2000 mm (-1500 / -1750 / -2000).

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

-	Fastening methods:

-	without fastening hole (-B0).

-	with fastening hole ø11.5 (-BB, standard). (Prepared for suspended installation by using an M8 threaded rod and an M8 nut to be provided on site.)

Accessories (at an extra charge):

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

Pressed bend BGE, according to DIN EN1506, suitable for connection to DIN ducts.

Product: SCHAKO type BGE-...

-	Nominal width:

-	NW 200 (-200)

-	NW 224 (-224)

-	NW 250 (-250)

-	NW 280 (-280)

-	NW 315 (-315)

-	Angle:

-	Angle 30° (-30).

-	Angle 45° (-45).

-	Angle 90° (-90).

Bends with different degree figures (a) are not available.

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

Accessories (at an extra charge):

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

Segment bend BSE, according to DIN EN1506, suitable for connection to DIN ducts.

Product: SCHAKO type BSE-...

-	Nominal width:

-	NW 355 (-355)

-	NW 400 (-400)

-	NW 450 (-450)

-	NW 500 (-500)

-	Angle:

-	Angle 15° (-15).

-	Angle 30° (-30).

-	Angle 45° (-45).

-	Angle 60° (-60).

-	Angle 90° (-90).

Bends with different degree figures (a) are not available.

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

Accessories (at an extra charge):

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

Symmetric reduction piece USE, according to DIN EN1506, suitable for connection to DIN ducts.

Product: SCHAKO type USE-...

-	Nominal width:

-	NW 224-200 (-224-200)

-	NW 250-200 (-250-200)

-	NW 280-200 (-280-200)

-	NW 315-200 (-315-200)

-	NW 315-250 (-315-250)

-	NW 355-250 (-355-250)

-	NW 400-250 (-400-250)

-	NW 400-315 (-400-315)

-	NW 450-280 (-450-280)

-	NW 450-315 (-450-315)

-	NW 500-315 (-500-315)

-	NW 500-400 (-500-400)

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

Accessories (at an extra charge):

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

Asymmetric reduction piece UAE, according to DIN EN1506, suitable for connection to DIN ducts.

Product: SCHAKO type UAE-...

-	Nominal width:

-	NW 224-200 (-224-200)

-	NW 250-200 (-250-200)

-	NW 280-200 (-280-200)

-	NW 315-200 (-315-200)

-	NW 315-250 (-315-250)

-	NW 355-250 (-355-250)

-	NW 400-250 (-400-250)

-	NW 400-315 (-400-315)

-	NW 450-280 (-450-280)

-	NW 450-315 (-450-315)

-	NW 500-315 (-500-315)

-	NW 500-400 (-500-400)

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

Accessories (at an extra charge):

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

T-piece ATE, according to DIN EN1506, suitable for connection to DIN ducts.

Product: SCHAKO type ATE-...

-	Nominal width:

-	NW 200-200 (-200-200)		-	NW 355-250 (-355-250)

-	NW 200-250 (-200-250) 		-	NW 355-315 (-355-315)

-	NW 200-315 (-200-315) 		-	NW 355-355 (-355-355)

-	NW 224-224 (-224-224) 		-	NW 355-500 (-355-500)

-	NW 224-250 (-224-250) 		-	NW 400-200 (-400-200)

-	NW 224-315 (-224-315)		-	NW 400-250 (-400-250)

-	NW 250-200 (-250-200) 		-	NW 400-315 (-400-315)

-	NW 250-250 (-250-250) 		-	NW 400-400 (-400-400)

-	NW 250-315 (-250-315) 		-	NW 400-500 (-400-500)

-	NW 250-400 (-250-400) 		-	NW 450-250 (-450-250)

-	NW 280-200 (-280-200) 		-	NW 450-315 (-450-315)

-	NW 280-280 (-280-280) 		-	NW 450-450 (-450-450)

-	NW 280-400 (-280-400) 		-	NW 450-500 (-450-500)

-	NW 315-200 (-315-200) 		-	NW 500-200 (-500-200)

-	NW 315-250 (-315-250) 		-	NW 500-250 (-500-250)

-	NW 315-315 (-315-315) 		-	NW 500-315 (-500-315)

-	NW 315-400 (-315-400) 		-	NW 500-400 (-500-400)

-	NW 315-500 (-315-500) 		-	NW 500-500 (-500-500)

-	NW 355-200 (-355-200)

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

Accessories (at an extra charge):

-	Rubber lip seal:

-	without rubber lip seal (-GD0) (standard).

-	with rubber lip seal (-GD1), on both sides, made of EPDM.

Push-on rosette SRO, suitable for connection to DIN ducts.

Product: SCHAKO type SRO-...

-	Nominal width:

-	NW 200 (-200)

-	NW 224 (-224)

-	NW 250 (-250)

-	NW 280 (-280)

-	NW 315 (-315)

-	NW 355 (-355)

-	NW 400 (-400)

-	NW 450 (-450)

-	NW 500 (-500)

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

Straight end cover EG, suitable for connection to DIN ducts.

Product: SCHAKO type EG-...

-	Nominal width:

-	NW 200 (-200)

-	NW 224 (-224)

-	NW 250 (-250)

-	NW 280 (-280)

-	NW 315 (-315)

-	NW 355 (-355)

-	NW 400 (-400)

-	NW 450 (-450)

-	NW 500 (-500)

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).

Connection sleeve MUF, suitable for connection to DIN ducts.

Product: SCHAKO type MUF-...

-	Nominal width:

-	NW 200 (-200)

-	NW 224 (-224)

-	NW 250 (-250)

-	NW 280 (-280)

-	NW 315 (-315)

-	NW 355 (-355)

-	NW 400 (-400)

-	NW 450 (-450)

-	NW 500 (-500)

-	Width:

-	70 mm (-070) (connecting round pipe/round pipe, dummy pipe/dummy pipe).

-	75 mm (-075) (connecting round pipe/dummy pipe with connecting piece d200-d224).

-	80 mm (-080) (connecting connecting piece/connecting piece d200-d224).

-	95 mm (-095) (connecting round pipe/dummy pipe with connecting piece d250-d355).

-	115 mm (-115) (connecting round pipe/dummy pipe with connecting piece d400-d500).

-	120 mm (-120) (connecting connecting piece/connecting piece d250-d355).

-	160 mm (-160) (connecting connecting piece/connecting piece d400-d500).

-	Material and paint:

-	Galvanised sheet steel (-SV-000) (at an extra charge).

-	Sheet steel (-SB-...):

-	painted to the RAL colour 9010 (white, standard) (-9010).

-	painted to a freely selectable RAL colour (-xxxx, always with 4 digits).